## Slide 1: WHY I SHOULD STICK MY NOSE IN OTHER PEOPLE’S BUSINESS
OR
WHY I SHOULD PARTICIPATE IN ALL PHASES OF THE DATA LIFE CYCLE

## Slide 2: Data Life Cycle
Planning
  Directed planning process
  Plan documents
  Contracting Services
Implementation
  Sampling – laboratory samples
  Analysis – laboratory analysis
Assessment
  Verification
  Validation
  Data quality assessment
Blame
Often the only places where lab personnel are considered key players

## Slide 3: MARLAP Warning
“Although the diagram represents the data life cycle in a linear fashion, it is important to note that the actual process is an iterative one, with feedback loops”
Summary
  Don’t go through the steps one at a time and think you are done

## Slide 4: Additional Warning
Steps appear compartmentalized
  Everyone has their own job
Steps truly overlap
  Everyone should stick their nose in everyone else’s business

## Slide 5: Example
Characterize a questionable set of soil piles
Large project with high visibility
Many other projects to be completed at the site

## Slide 6: Objectives
Stakeholders meet to determine objectives
  Determine if soil piles are dangerous to the public
  Determine exactly what is in the piles
  Efficacy of field testing methods at site
    Can XRF and ISOCS be used to save money on future projects?
    Determine efficacy as a screening tool
    Possible to use in risk assessment?

## Slide 7: Planning
Many planning meetings held
  Want to get everything just right
Carefully select an appropriate sampling design
  Use splits to be able to compare analytical lab measurements with XRF and ISOCS results
Statistical analysis thoroughly discussed and evaluated before a single sample was collected

## Slide 8: Safety Question
Measurements obtained
Soil piles are safe
  All analytes of concern present in amounts well below action limits
Conclusions based on lab techniques
  Highly defensible

## Slide 9: XRF Results
Measured barium, chromium, lead, and uranium
Relative error of upper confidence limits (UCLs) as large as 690% compared to laboratory data
5% of lead measurements were false positives relative to the no action limit
16% of uranium measurements were false positives relative to the no action limit
56% of uranium measurements were false negatives relative to background
Chromium was not detected by XRF at background levels

## Slide 10: ISOCS Results
Measured Cs-137 and U-238
Relative error of upper confidence limits (UCLs) as large as 540% compared to laboratory data
60% false negative rate relative to the no action limit for Cs-137
Unable to detect U-238 at background levels
Unable to detect U-238 at the no action limit

## Slide 11: Conclusions from Results
XRF and ISOCS data cannot be used to compute UCLs
Data were not adequately conclusive to determine if XRF and ISOCS were sufficient for screening

## Slide 12: What Now?
Stakeholders were certain results would be better
Decided not to use XRF and ISOCS on future projects

## Slide 13: Fast Forward - Lab
Several months after project completed
  Conversed with a subject matter expert from a laboratory familiar with the project
  Insisted that better results should have been obtained
  Explained sample preparation methods that may have produced data sufficiently accurate to compute UCLs
  Questioned whether field workers properly performed XRF and ISOCs

## Slide 14: Fast Forward - Field
Spoke with person in charge of field sampling
  Followed instructions exactly as outlined in vendor instructions
    Not as rigorous as the method outlined by lab subject matter expert
  Spoke with lab prior to sampling
    Lab insisted on all or nothing – they wanted complete control or did not want to help
    Too expensive so knowledge from lab personnel not available
  Unaware that XRF and ISOCS data were to be used to compute UCLs
    Believed that XRF and ISOCS data were only to be qualitative

## Slide 15: Breakdown
Extensive planning, but …
  Laboratory personnel and field workers absent from all planning
  Objectives not conveyed to those gathering the data
  Laboratory personnel not consulted to ensure best practices were used in the field
  Vendor information not adequate for data needs

## Slide 16: Missing Pieces
Data needs were specific but lab was not consulted on proper protocol for data needs
Laboratory personnel were unwilling to provide information essential to project success when approached by field workers
Data needs were not conveyed to those collecting and analyzing the data

## Slide 17: Lessons Learned
What about next time?
  Laboratory personnel need to be involved in planning meetings
  Laboratory personnel should meet with field samplers to ensure that field methods are executed properly for data needs
  Project planners need to involve key personnel from all phases

## Slide 18: Own Your Expertise
Don’t wait to be asked
  Nobody will ask you because they don’t know they need you
Recognize that you may not be given the control you want or need
  Be willing to help however you can
Don’t be afraid to be pushy
  They don’t know they need your help
  They don’t know how you can help

## Slide 19: Contact Information
Jill Lundell, PStat®
  Senior Statistician, Portage, Inc.
  Phone: (208) 419-4163
  Cell: (208) 360-5475
  Email: jlundell@portageinc.com
Berta Oates
  Carlsbad Technical Assistance Contract (Portage, Inc.)
  Phone: (801) 782-5179
  Cell: (801) 814-5082
  Email: boates@portageinc.com